## Slide 1
HO CHI MINH UNIVERSITY OF TECHNOLOGY
FACULTY OF TRANSPORTATION ENGINEERING
DEPARTMENT OF AUTOMOTIVE AND ENGINE
CAPSTONE PROJECT
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
STUDENT: Ho Binh Minh - ID: 1852169
INSTRUCTOR: Ph.D. Ngo Dac Viet
Ph.D. Tran Dang Long
DATE: 25/05/2023
TOPIC CODE: SVOISPLV-2022-KTGT-32

## Slide 2
Introduction
CONTENTS
Theoretical basis
Implementation process
Conclusion and future work
1
3
4
2
5
Result and disscussion
1
Ho Chi Minh University of Technology – 2023/05
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
Notes: 3. Mô tả bài toán (sử dụng mô phỏng)
4. Cases (các trường hợp)

## Slide 3
Introduction
CONTENTS
Theoretical basis
Implementation process
Conclusion and future work
1
3
4
2
5
Result and discussion
1.1
1.2
Thesis objectives & limitations
2
Ho Chi Minh University of Technology – 2023/01
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
Working conditions & Technical requirements
V model
1.3
Notes: 3. Mô tả bài toán (sử dụng mô phỏng)
4. Cases (các trường hợp)

## Slide 4
1. INTRODUCTION
1.1 Thesis objectives & limitations
Thesis’s objectives: Modeling and simulation the resistance torque for specific wheel alignment in the Electric Power Steering system by using Matlab/Simulink and its application.
Find out how wheel alignment can affect the resistance torque in the steering mechanism especially in the EPS system.
Build the complete model of the resistance torque between the tire forces and road.
3
Ho Chi Minh University of Technology – 2023/01
Idea:
Using Matlab/Simulink environment to simulate and verify the response of the system.
Limitations:
The tire turns right only.
Longitudinal force, lateral force, rolling resistance force, normal force and no more internal and external force.
Hypothesis:
The model is developed by assuming that the wheels are in contact with the road surface.

## Slide 5
1. INTRODUCTION
1.2 Working conditions and technical requirements
Working conditions:
- Continuously change to adapt to variable driving conditions.
Technical requirements:
- Working normally in above conditions.
- Measuring resistance torque range: The error within the allowable range.
4
Ho Chi Minh University of Technology – 2023/01

## Slide 6
1. INTRODUCTION
1.3 V model
4
Ho Chi Minh University of Technology – 2023/01

## Slide 7
Introduction
CONTENTS
Theoretical basis
Implementation process
Conclusion and future work
1
3
4
2
5
Result and disscussion
Wheel alignment
2.1
2.2
Tire force equations
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
Total resistance torque equations
2.3
5
Ho Chi Minh University of Technology – 2023/01

## Slide 8
2.1 Wheel alignment
2. THEORETICAL BASIS
6
Ho Chi Minh University of Technology – 2023/01
Figure: Overall in Caster angle
Figure: Kingpin angle and its scrub radius
Figure: Camber angle at front view
Caster angle is the angular displacement of the steering axis from the vertical axis of a steered wheel.
Kingpin angle is a measure of the angle of the suspension steer axis relative to vertical at front view.
Camber angle is is the angle between the vertical axis of a wheel and the vertical axis of the vehicle when viewed from the front or rear

## Slide 9
2.2 Tire force equations
2. THEORETICAL BASIS
7
Ho Chi Minh University of Technology – 2023/01
+
Rolling resistance force (Fr)
Figure: Overall tire forces and Kingpin angle
m: mass of the vehicle (kg)
g = 9.8: gravitational acceleration (m/
: Cornering stiffness of the tire (N/rad)
= 0.011 : rolling resistance coefficient
: Longitudinal friction coefficient
: Camber stiffness of the tire

## Slide 10
2.3 Total resistance torque equations
2. THEORETICAL BASIS
8
Ho Chi Minh University of Technology – 2023/01
Moment arm
Applied forces
Input
Input
Input
Input
Total resistance torque
Input
Operation flow

## Slide 11
2.3 Total resistance torque equations
2. THEORETICAL BASIS
9
Ho Chi Minh University of Technology – 2023/01

## Slide 12
2.3 Total resistance torque equations
2. THEORETICAL BASIS
10
Ho Chi Minh University of Technology – 2023/01

## Slide 13
2.3 Total resistance torque equations
2. THEORETICAL BASIS
11
Ho Chi Minh University of Technology – 2023/01

## Slide 14
2.3 Total resistance torque equations
2. THEORETICAL BASIS
12
Ho Chi Minh University of Technology – 2023/01

## Slide 15
Introduction
CONTENTS
Theoretical basis
Implementation process
Conclusion and future work
1
3
4
2
5
Result and disscussion
3.1
Modeling the total resistance torque by lateral forces FY
3.2
Modeling the total resistance torque by longitudinal forces FX
Modeling the total resistance torque by normal force FZ
3.3
13
Ho Chi Minh University of Technology – 2023/01
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
Notes: 3. Mô tả bài toán (sử dụng mô phỏng)
4. Cases (các trường hợp)

## Slide 16
3. IMPLEMENTATION PROCESS
3.1 Modeling the total resistance torque by longitudinal forces FX
14
Ho Chi Minh University of Technology – 2023/01
Moment arm
Total applied force

## Slide 17
3. IMPLEMENTATION PROCESS
3.2 Modeling the total resistance torque by lateral forces FY
15
Ho Chi Minh University of Technology – 2023/01
Moment arm
Total applied force

## Slide 18
3. IMPLEMENTATION PROCESS
3.3 Modeling the total resistance torque by normal forces FZ
16
Ho Chi Minh University of Technology – 2023/01
Moment arm
Total applied force

## Slide 19
Introduction
CONTENTS
Key problems
Implementation process
Conclusion and future work
1
3
4
2
5
Result and disscussion
4.1
4.2
4.3
17
Ho Chi Minh University of Technology – 2023/01
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
Vehicle mass
Vehicle velocity
Wheel alignment
4.4
Steering wheel angle
Notes: 3. Mô tả bài toán (sử dụng mô phỏng)
4. Cases (các trường hợp)

## Slide 20
4. Result and disscussion
4.1 Vehicle mass
18
Ho Chi Minh University of Technology – 2023/01
Total resistance torque by Fz increases slowly when vehicle mass increases.
Total resistance torque by FY and FX increase quickly when vehicle mass increases.
Total resistance torque increases when vehicle mass increases.
Vehicle mass has strong influence on total resistance torque

## Slide 21
4. Result and disscussion
4.2 Vehicle velocity
19
Ho Chi Minh University of Technology – 2023/01
Total resistance torque decreases when vehicle speed increases
Decrease quickly at low speed and gradually higher speed range
Total resistance torque by Fz is stable when vehicle speed increases
Total resistance torque by FX gradually increases while resistance torque by FY rapidly decreases when vehicle vehicle increases
Vehicle velocity has influence on total resistance torque

## Slide 22
4. Result and disscussion
20
Ho Chi Minh University of Technology – 2023/01
Total resistance torque also decrease when changing both vehicle mass and vehicle speed
4.1 + 4.2: Vehicle mass and vehicle speed

## Slide 23
4. Result and disscussion
21
Ho Chi Minh University of Technology – 2023/01
4.3: Wheel alignment
Total resistance torque caused FY is almost stable when Kingpin angle increases.
Total resistance torque caused FZ and FX rapidly increases when Kingpin angle increases.
Total resistance torque increases when Kingpin angle increases
Changing in Kingpin vehicle wheel alignment
Kingpin angle has strong influence on total resistance torque

## Slide 24
4. Result and disscussion
22
Ho Chi Minh University of Technology – 2023/01
4.3: Wheel alignment
Changing in Caster vehicle wheel alignment
Total resistance torque caused FX and FZ are almost stable when Caster angle increases.
Total resistance torque caused FY increase when Caster angle increases.
Total resistance torque increases when Caster angle increases
Caster angle has slight effect on total resistance torque

## Slide 25
4. Result and disscussion
23
Ho Chi Minh University of Technology – 2023/01
4.3: Wheel alignment
Changing in Camber vehicle wheel alignment
Total resistance torque increases when Camber angle increases.
Total resistance torque caused FZ is constant when Camber angle increases.
While total resistance torque caused FY rapidly increases, the total resistance torque caused by FX quickly decreases when Camber angle increases.
Camber angle has impact on total resistance torque

## Slide 26
4. Result and disscussion
24
Ho Chi Minh University of Technology – 2023/01
4.4 Steering wheel angle
Increase steering wheel angle, increase the total resistance torque
Vehicle steering wheel angle has huge impact on total resistance torque

## Slide 27
4. Result and disscussion
24
Ho Chi Minh University of Technology – 2023/01
4.4 Steering wheel angle
Increase steering wheel angle, increase the total resistance torque
Vehicle steering wheel angle has huge impact on total resistance torque

## Slide 28
Introduction
CONTENTS
Theoretical basis
Implementation process
Conclusion and future work
1
3
4
2
5
Result and disscussion
25
Ho Chi Minh University of Technology – 2023/01
MODELING AND SIMULATION THE RESISTANCE TORQUE FOR SPECIFIC WHEEL ALIGNMENT IN THE ELECTRIC POWER STEERING SYSTEM BY USING MATLAB/SIMULINK AND ITS APPLICATION
Notes: 3. Mô tả bài toán (sử dụng mô phỏng)
4. Cases (các trường hợp)

## Slide 29
5. CONCLUSION & FUTURE WORK
26
Ho Chi Minh University of Technology – 2023/01
CONCLUSION
FUTURE WORKS
All the steering resistance torque conveys are clearly mentioned in this Capstone project. Moreover, a total steering resistance torque model of a power steering system is built exactly by applying the above knowledge: numerical equations and relevant factors. It can also be used for the design of other power steering systems, thanks to the resistance torque model to calculate the appropriate assist torque in different driving conditions.
The main conclusion obtained in this Capstone project is how the wheel alignment especially the Caster angle, Kingpin angle, and Camber angle affects to the resistance moment.
It is recommended to develop this steering mechanism model and go further to simulate different situations by assisting simulators such as Matlab/Simulink based on all relevant theories mentioned in this Capstone project

## Slide 30
References
27
Ho Chi Minh University of Technology – 2023/01
Jazar, R. N. (2017). Vehicle Dynamics: Theory and Application (3rd ed. 2017). Springer.
Lenzo, B. (2021). Vehicle Dynamics: Fundamentals and Ultimate Trends (CISM International Centre for Mechanical Sciences, 603) (1st ed. 2022). Springer.
Cossalter, V. (2006). Motorcycle Dynamics (2nd ed.). Lulu.com.
Reimpell, J., Stoll, H., Betzler, J. W., & Engineers, S. O. A. (2022). The Automotive Chassis: Engineering Principles (2nd ed.). Society of Automotive Engineers.
American Association of State Highway and Transportation Officials. (2022). A Policy on Geometric Design of Highways and Streets 2011 (6th ed.). Amer Assn of State Hwy.
Wikipedia contributors. (2022, September 13). Vehicle dynamics. Wikipedia. https://en.wikipedia.org/wiki/Vehicle_dynamics
Pauwelussen, J. (2014). Essentials of Vehicle Dynamics (1st ed.). Butterworth-Heinemann.
Hu, C. H. (2008). Modeling and Simulation of Automotive Electric Power Steering System. 2008 Second International Symposium on Intelligent Information Technology Application. https://doi.org/10.1109/iita.2008.51